## Slide 1: ICSE 6222: Mobile Tel. Tech

## Slide 2: History of Mobile Data Networks
Remember that phones were originally designed for calls

## Slide 3: Cellular Network Basics
There are many types of cellular services; before delving into details, focus on basics (helps navigate the “acronym soup”)
Cellular network/telephony is a radio-based technology; radio waves are electromagnetic waves that antennas propagate
Most signals are in the 850 MHz, 900 MHz, 1800 MHz, and 1900 MHz frequency bands
Cell phones operate in this frequency range (note the logarithmic scale)

## Slide 4: Cellular Network Generations
It is useful to think of cellular Network/telephony in terms of generations:
  0G: Briefcase-size mobile radio telephones
  1G: Analog cellular telephony
  2G: Digital cellular telephony
  3G: High-speed digital cellular telephony (including video telephony)
  LTE (4G): IP-based “anytime, anywhere” voice, data, and multimedia telephony at faster data rates than 3G

## Slide 5: Evolution of Cellular Networks
1G
2G
3G
4G
2.5G

## Slide 6: Cellular Network
Base stations transmit to and receive from mobiles at the assigned spectrum
  Multiple base stations use the same spectrum (spectral reuse)
The service area of each base station is called a cell
Each mobile terminal is typically served by the ‘closest’ base stations
  Handoff when terminals move

## Slide 7: The Multiple Access Problem
The base stations need to serve many mobile terminals at the same time (both downlink and uplink)
All mobiles in the cell need to transmit to the base station
Interference among different senders and receivers
So we need multiple access scheme

## Slide 8: Multiple Access Schemes
Frequency Division Multiple Access (FDMA)
Time Division Multiple Access (TDMA)
Code Division Multiple Access (CDMA)
3 orthogonal Schemes:

## Slide 9: Frequency Division Multiple Access
Each mobile is assigned a separate frequency channel for a call
Guard band is required to prevent adjacent channel interference
Usually, one downlink band and one uplink band
Different cellular network protocols use different frequencies
Frequency is precious and scare – we are running out of it
  Cognitive radio
frequency

## Slide 10: Time Division Multiple Access
Time is divided into slots and only one mobile terminal transmits during each slot
  Like during the lecture, only one can talk, but others may take the floor in turn
Each user is given a specific slot. No competition in cellular network
  Unlike Carrier Sensing Multiple Access (CSMA) in WiFi
Guard time – signal transmitted by mobile terminals at different locations do no arrive at the base station at the same time

## Slide 11: Code Division Multiple Access
Use of orthogonal codes to separate different transmissions
Each symbol of bit is transmitted as a larger number of bits using the user specific code – Spreading
  Bandwidth occupied by the signal is much larger than the information transmission rate
  But all users use the same frequency band together
Orthogonal among users

## Slide 12: Why am I telling you this?
…and cell networks (pre-LTE) were not designed for IP
Instead, optimized for
  Circuit-switched
  Low bitrate (calls/text)
  Charging customers, allowing connections from any cell provider
The performance we get out of cell networks is intimately tied to network design

## Slide 13: Wired networks are relatively simple
DSL Access Multiplexer:
Separates voice and data
Broadband Remote Access Server:
Bridge between layer 2 and 3, sits in core

## Slide 14: “Simplified” view of 3G
NodeB & Base Station Controller:
Converts RF to wired
Mobile switching center:
Analog to digital
Serving GPRS Support Node:
Move IP packets to/from radio network
Gateway GPRS Support Node:
Route to/from the Interet
$

## Slide 15: Packet switched vs circuit switched
3G and earlier maintains two data paths
  Circuit switched: Phone calls (8kbps) and SMS/MMS
  Packet switched: All IP data

## Slide 16: Packet switched vs circuit switched
LTE uses “all in one” approach
  Everything over IP, including voice
  S-GW (Serving Gateway) replaced SGSN, P-GW replaces GGSN

## Slide 17: Backward compatibility

## Slide 18: Mobile Architecture in practice
RNC/NodeB: 1000s
SGSNs/S-GWs: 10s or 100s
GGSN/P-GWs: < 10
  Why is this a problem?

## Slide 19: Very few GGSNs for a large region

## Slide 20: Implication: Path Inflation
Path inflation: Two nearby hosts are connected by a geographically circuitous IP path
  Can be caused by
    Carrier path
    Interdomain policy
    Lack of nearby peering points

## Slide 21: Path Inflation Example: Ingress

## Slide 22: Path Inflation Example: Peering

## Slide 23: Inflation breakdown for AT&T

## Slide 24: Wireless/Radio Issues
Conflicting goals
  IP application assume “always on” connectivity
  Radio consumes large amounts of power
  How to balance the two?
Compromise in UMTS networks: 3 power states
  Idle: No data channel, only paging, almost no power
  FACH: Shared, low-speed channel, low power
  DCH: Dedicated channel, high speed, high power

## Slide 25: Issues with this approach
State promotions have promotion delay
State demotions incur tail times
DCH
FACH
IDLE
Send/Recv any data
Queue > threshold
Idle for 12 s
Idle for 5 s
800 mW
High Bandwidth
460 mW
Low Bandwidth
No Power
No BW

## Slide 26: Delays add up…
Delay to send a packet
Delay to save power

## Slide 27: … to inefficiency
Inefficient radio utilization (34% power/channel)

## Slide 28: LTE Key Features
Uses Multi-input Multi-output (MIMO) for enhanced throughput
Reduced power consumption
Higher RF power amplifier efficiency (less battery power used by handsets)
Lower latency to get access to the medium
Performance sometimes better than WiFi!

## Slide 29: Middleboxes in Mobile Networks
Carrier-grade NAT
  Devices often assigned private IPs
  Firewalled connections
Content optimizers
  Split TCP connections
    Why?
  Compression and caching
  Other strange behavior
How might we measure
these?
Mobile networks
Mobile networks